## Slide 1
high efficiency
hjt module

## Slide 2
The Power of iPower

## Slide 3
HJT Technical Advantage
Mounting System Matching
Lowest Degradation
No PID, LID effect
Low temperature coefficient
High Bifaciality
Excellent Low Irradiance Response
Higher Energy Production
Higher Reliability
Non-Destructive Cutting Technology
Low-Temperature Welding
Technical Characteristics of Shingled Module
Framed Double Glass Design

## Slide 4
HJT No LID/PID Effect
Chart: 
| 0 | 5 | 17 | 37.799999999999997 | 57.2 | 70.400000000000006 | 86.4 | 100.3 | 113.3
P型多晶 | 0 | 1.28 | 1.58 | 1.22 | 1.67 | 1.44 | 1.69 | 1.76 | 1.83
N型单晶 | 0 | -0.13 | -0.15 | -0.14 | 0.12 | 0.09 | -0.1 | 0.15 | 0.08
Note: LID: P-type cells doped with boron and oxygen and metal impurities light irradiation to form compounds, resulting in the cell's efficiency decay;
N-type silicon wafers are mainly doped with phosphorus, which is not easy to form compounds in sunlight.
1、The HJT cell is designed with conductive TCO surface and insulation-free layer, so there is no build-up surface layer charge.
2、25 years of HJT module application with no customer feedback of PID occurrences.
3、No PID occurrences after in-house and third party reliability testing.
Data Source: Panasonic

## Slide 5
Lowest Degradation
Akcome's laminated module products use HJT cells, which have better attenuation resistance, high efficiency, stable and long-lasting power generation, while Hi-chaser promises to provide the best quality assurance to ensure maximum customer value.
TCO film in HJT module prevents charge accumulation on the surface, resulting high resistance to PID;
LID (light-induced degradation) is mainly formed by B-O complex in silicon wafer. Because of the absence of B-O complex in n-type silicons, the LID effect is less.
98%
0.25%/Year
Standard module
HJT shingled module
92%
90.75%
2%
-0.25%
Attenuation rate
in the first year
Linear annual docay
98%
0.55%/Year
84.8%
Low temperature coefficient and high bifaciality performance allows HJT module to bring more energy yield. According to the existing power warranty curve, HJT module has higher power retention rate than that of Mono PERC. Higher power retention rate brings more energy yields.

## Slide 6
Lower Temperature Coefficients
Chart: HJT VS PERC module output power under varied operating temperatures
| 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70
perc | 1.038 | 1.0342 | 1.0304 | 1.0266 | 1.0228 | 1.019 | 1.0152 | 1.0114 | 1.0076 | 1.0038 | 1 | 0.9962 | 0.9924 | 0.9886 | 0.9848 | 0.981 | 0.9772 | 0.9734 | 0.9696 | 0.9658 | 0.962 | 0.9582 | 0.9544 | 0.9506 | 0.9468 | 0.943 | 0.9392 | 0.9354 | 0.9316 | 0.9278 | 0.924 | 0.9202 | 0.9164 | 0.9126 | 0.9088 | 0.905 | 0.9012 | 0.8974 | 0.8936 | 0.8898 | 0.886 | 0.8822 | 0.8784 | 0.8746 | 0.8708 | 0.867 | 0.8632 | 0.8594 | 0.8556 | 0.8518 | 0.848 | 0.8442 | 0.8404 | 0.8366 | 0.8328 | 0.829
HJT | 1.024 | 1.0216 | 1.0192 | 1.0168 | 1.0144 | 1.012 | 1.0096 | 1.0072 | 1.0048 | 1.0024 | 1 | 0.9976 | 0.9952 | 0.9928 | 0.9904 | 0.988 | 0.9856 | 0.9832 | 0.9808 | 0.9784 | 0.976 | 0.9736 | 0.9712 | 0.9688 | 0.9664 | 0.964 | 0.9616 | 0.9592 | 0.9568 | 0.9544 | 0.952 | 0.9496 | 0.9472 | 0.9448 | 0.9424 | 0.94 | 0.9376 | 0.9352 | 0.9328 | 0.9304 | 0.928 | 0.9256 | 0.9232 | 0.9208 | 0.9184 | 0.916 | 0.9136 | 0.9112 | 0.9088 | 0.9064 | 0.904 | 0.9016 | 0.8992 | 0.8968 | 0.8944 | 0.892
1.10
1.05
1.00
0.90
0.85
0.80
Compared to PERC module, HJT features lower power temperature coefficient and higher output power. It is about 4.9% more efficient in power output than PERC module under 60℃ operation temperature.
HJT demonstrates unique advantages in high temperature/high irradiance area.
Power generation gain of up to 10% or more can be achieved in summer when the module temperature is above 75 degrees.
Data Source: Panasonic

## Slide 7
High Bifaciality
Note: Bifaciality will be affected by grid width of the back panel, bifaciality of the cell itself and test method etc, which shall be subject to Akcome’s design and test.
75-80%
85-90%
65-70%
Cell：MONO-Perc
Type: Mesh-like double glass
Cell：N-TYPE Topcon
Type：Mesh-like double glass
Cell：
Type：Mesh-like double glass
Bifaciality：
Bifaciality：
Bifaciality：
HJT
HJT is considered one of the top cell technologies with highest bifaciality. Higher bifaciality allows more energy yield on the back.
Generally, it enables 5%-30% energy gain on the back, depending on the factors such as ground reflection, region type etc.

## Slide 8
Excellent Low Irradiance Response
Due to the high Minority carriers life time of N-type substrate materials, N-type crystalline silicon modules demonstrate better power generation characteristics than conventional P-type crystalline silicon modules under low light.

## Slide 9
The effective power generation time of HJT is 11.07% more than the effective power generation time of conventional cells.
11.07%
Higher Energy Production

## Slide 10
Higher Reliability
Chart: Reliability of HJT Bifacial Double Glass Module
| PID192h | LID60kwh | DH3000 | TC100+HF20 | TC600 | UV60kwh | ML | Hot spot
衰减 | -0.0173 | 0.0118 | -0.0355 | -0.0226 | -0.027 | -0.0186 | -0.0061 | -0.0021
All degradation after test is much lower than IEC standard.

## Slide 11
Non-Destructive Cutting Technology
Rough surface resulting 80-120μm heat affected area
Smooth cutting surface with zero heat-affected area
VS
Figure 2: Procedures of non-destructive cutting
Figure 1: Working principle of non-destructive cutting
Figure 3：Comparison of two cutting solutions of 166mm Mono PERC (Data source: Delong)
166mm Single Glass 9BB Half-Cell （Solar cell：22.5%） | Traditional Cutting | Non-destructive cutting technology
 | 447.17 | 448.59
Increase | 1.4W | 
Traditional Cutting
Non-destructive
cutting technology
Non-destructive cutting technology：Laser localized heating and supporting cooling technology are used to form gradient temperature within the material, which formulates the thermal stress to force the material to crack.
Advantages: Smooth surface by non-destructive cutting; no heat affected area; less cutting effect to cell efficiency.

## Slide 12
Low-Temperature Welding
Process of HJT Low Temperature Welding VS. PERC cell Traditional Welding
Round wire welding (Tin-Lead-Bismuth)
+
165-190℃
Welding
Low-temperature welding flux
HJT cell
Perc Cell
HJT Bifacial Double Glass Module
Round wire welding strip(Tin-Lead)
MBB welding flux
+
210-230℃
Welding
Perc Bifacial Double Glass Module
Reliability of HJT low-temperature welding VS. PERC welding
HJT cells are welded with low-temperature welding strip and welding flux. Bring much lower damage for the cells.

## Slide 13
Technical Characteristics of Shingled Module
Akcome's stack welding technology uses the lamination solution after slicing to eliminate the internal cell gap, maximize the light receiving area of the module, and increase the module conversion efficiency by 1% over conventional multi-master grid products.

## Slide 14
Mounting System Matching
Multiple application
Efficiency improvements help reduce system costs
Full range of mounting system solutions

## Slide 15
iPower Product Series
Application Scenario | cell size | Layout | Component size | Weight |  | 2021 Q4 | 2022 Q1 | 2022 Q2 | 2022 Q3 | 2022 Q4
ground power plants | 158.75mm | 60-pattern | 1714*1010*30 | 22.4 |  | 360 | 360 | 365 | 365 | 370
 |  | 72-pattern | 2030*1010*30 | 26.8 |  | 435 | 435 | 440 | 440 | 445
 | 166mm | 60-pattern | 1755*1038*30 | 22.8 |  | 395 | 395 | 400 | 400 | 405
 |  | 72-pattern | 2094*1038*30 | 27.0 |  | 475 | 475 | 480 | 480 | 485
 | 210mm | 50-pattern | 2187*1102*35 | 30.3 |  |  | 525 | 525 | 530 | 530
 |  | 55-pattern | 2384*1096*35 | 32.6 |  |  | 575 | 575 | 580 | 580
 |  | 60-pattern | 2172*1303*35 | 35.3 |  |  | 625 | 625 | 630 | 630
 |  | 66-pattern | 2384*1303*35 | 38.7 |  |  | 685 | 685 | 690 | 690
distributed power plants | 210mm | 40-pattern | 1754*1096*30 |  | 23.6 |  | 420 | 420 | 425 | 425

## Slide 16
2021主推版型
72-Pattern
158.75mm
*STC(Standard Test Condition): Irradiance 1000w/m2, Cell Temperature 25℃, Air Mass1.5
Maximum Power Pmax (W)
Power Tolerance(%)
Maximum Power Voltage Vmp(V)
Maximum Power Current Imp(A)
Open Circuit Voltage Voc(V)
Short Circuit Current Isc(A)
module efficiency(%)
module size(mm)
430W
0~+3%
45.46
9.46
54.00
10.08
20.98
2030*1010*30
Temperature Coefficients of PmpTemperature Coefficients of Voc
Temperature Coefficients of Isc
-0.24%/℃
-0.22%/℃ +0.047%/℃
72-Pattern
166mm
470W
0~+3%
45.70
10.28
53.95
11.02
21.62
2094*1038*30
-0.24%/℃
-0.22%/℃ +0.047%/℃
55-Pattern
210mm
575W
0~+3%
35.45
16.22
41.33
17.22
22.00
2384*1096*35
-0.24%/℃
-0.22%/℃ +0.047%/℃
66-Pattern
210mm
685W
0~+3%
43.32
16.19
49.40
17.20
22.10
2384*1303*35
-0.24%/℃
-0.21%/℃ +0.047%/℃

## Slide 17
Configuration version
Residential
Commercial
iPower 390/395/400
iPower 415/420/425
iPower 430/435/440
iPower 470/475/480
Utility
iPower 570/575/580
iPower 520/525/530
iPower 620/625/630
iPower 680/685/690

## Slide 18
Benchmarking Module Details
Higher module efficiency
Compatible with distributed
power system on rooftops and large-scale ground-mounted power plants
Higher generation revenue
Lower Full life cycle cost of electricity
Cell size/Layout | 166mm /120pcs |  | 210mm /132pcs |  | 158.75mm/ 132pcs | 210mm/ 120pcs
Module | Akcome HJT Half-cut | L Brand Perc Half-cut | Akcome HJT Half-cut | T Brand Perc Half-cut | Akcome HJT shingled all black | T Brand Perc Half-cut
Power（W） | 395 | 375 | 700 | 670 | 425 | 415
Size (Length*width* Height/mm) | 1791*1048*30 | 1755*1038*35 | 2384*1303*35 | 2384*1303*35 | 1690*1160*30 | 1754*1096*30
Efficiency(%） | 21.04% | 20.59% | 22.53% | 21.57% | 21.68% | 20.42%
Bifaciality Factor(%) | 85% | / | 85% | 70% | 85% | /
Degradation Rate(%） | 2% for the first year, and 0.25% annually since the 2nd year | 2% for the first year, and 0.55% annually since the 2nd year | 2% for the first year, and 0.25% annually since the 2nd year | 2% for the first year, and 0.55% annually since the 2nd year | 2% for the first year, and 0.25% annually since the 2nd year | 2% for the first year, and 0.55% annually since the 2nd year
Temperature Coefficients(%/℃) | -0.24% | -0.35% | -0.24% | -0.34% | -0.24% | -0.34%

## Slide 19
Application Scenario Analysis②-Ground Power Plant
Ulan，Qinghai，China
100000㎡(250*400m)Fixed area
Adopts Akcome Fixed Mounting System
Improved energy yield for 30 years：
Land cost saving：
Variable BOS cost：
LCOE reduce：
+9.20%
-6.00%
+1.70%
-4.50%
BOS cost analysis Fixed adjustable mounting system , longitudinal double row 2P,30% sand reflectivity Extremely low Environmental Temperature -22℃ |  |  |  |  | 
Cell size/Layout |  | 166mm /120pcs |  | 210mm /132pcs | 
Module |  | Akcome HJT Half-cut | L Brand Perc Half-cut | Akcome HJT Half-cut | T Brand Perc Half-cut
Power（W） |  | 395 | 375 | 700 | 670
Efficiency（%） |  | 21.04% | 20.59% | 22.53% | 21.57%
Power generation | 30-year power generation with the same area | 54.3 | 49.7 | 54.0 | 50.9
 | 30-year cumulative increase rate | 9.20% | benchmark | 6.10% | benchmark
BOS cost | Land cost | -6.00% | benchmark | -4.30% | benchmark
 | Variable BOS cost | 1.70% | benchmark | -2.10% | benchmark
LCOE | LCOE | 0.2882 | 0.3013 | 0.2841 | 0.2929
 | LCOE calculation | -4.50% | benchmark | -3.10% | benchmark

## Slide 20
Application Scenario Analysis①-Ground Power Plant
BOS cost analysis Fixed adjustable mounting system , longitudinal double row 2P,30% sand reflectivity， Extremely low Environmental Temperature 9℃ |  |  |  |  | 
Cell size/Layout |  | 166mm /120pcs |  | 210mm /132pcs | 
Module |  | Akcome HJT Half-cut | L Brand Perc Half-cut | Akcome HJT Half-cut | T Brand Perc Half-cut
Power（W） |  | 395 | 375 | 700 | 670
conversion efficiency（%） |  | 21.04% | 20.59% | 22.53% | 21.57%
Power generation | 30-year power generation with the same area | 52.2 | 47 | 51.5 | 47.7
 | 30-year cumulative increase rate | 11.10% | benchmark | 8.10% | Benchmark
BOS cost | Land cost | -6.00% | benchmark | -4.30% | Benchmark
 | Variable BOS cost | 4.5% | benchmark | -2.2% | benchmark
LCOE | LCOE | 0.2933 | 0.3097 | 0.2921 | 0.3051
 | LCOE calculation | -5.6% | benchmark | -4.5% | benchmark
Abu Dhabi，Middle East
100000㎡(250*400m)Fixed area
Adopts Akcome Fixed Mounting System
Improved energy yield for 30 years：
Land cost saving：
Variable BOS cost：
LCOE reduce：
+11.10%
-6.00%
+4.50%
-5.60%

## Slide 21
Application Scenario Analysis③-Roof Power Plant
BOS cost analysis Fixed adjustable roof mounting system , longitudinal double row 2P,70% sand reflectivity Extremely low Environmental Temperature -5℃ |  |  |  | 
Module | I POWER HJT Half-cut | L Brand Perc Half-cut | I POWER HJT shingled all black | T Brand Perc Half-cut
Cell size/Layout | 166mm/120pcs | 166mm/120pcs | 158.75mm/132pcs | 210mm/120pcs
Power（W） | 395 | 375 | 425 | 415
Efficiency（%） | 21.04% | 20.59% | 21.68% | 20.42%
30-year power generation with the same area | 4.5 | 4.1 | 4.5 | 3.9
30-year cumulative increase rate | 9.40% | benchmark | 14.50% | benchmark
Roof cost | 4.1736 | 3.957 | 4.1374 | 3.8591
LCOE | 0.4173 | 0.4427 | 0.4166 | 0.4391
LCOE calculation | -6.10% | benchmark | -5.40% | benchmark
Zhangjiagang，Jiangsu，China
10000㎡(100*100m) Fixed area，Industrial and commercial roof
Adopts Akcome Fixed Mounting System
Improved energy yield for 30 years：
LCOE reduce：
+14.50%
-6.10%

## Slide 22
HJT Project Case
Photovoltaic Poverty Alleviation (PVPA) project -- Longchuan County 5.19MW
Residential DPV project -- Handan, Hebei 30kW
industrial and commercial DPV project -- Taixing Industrial Park 1MW

## Slide 23
Real Data of HJT Module Application
4.26 MW HJT PV Project,
Power Generation Application Leading Base –
Baicheng, Jilin

## Slide 24
Web: www.ipss.co.kr
Korea distributor : ips system co,.ltd
Partner :